## Slide 1
Fiber-to-Detector 2D Coupling: Model & Concepts
Geometry
  SMF-28 fiber emits along +x; detector active face points -z (downward)
  Only diverging rays from the Gaussian tail reach the detector
  2D cross-section in the x-z plane; detector length = 1 mm
Factors in the Model
  1. Gaussian beam angular profile G(th) = exp(-2 th^2 / th0^2)
  2. Snell refraction at fiber exit (n_core > n_air -> beam widens)
  3. Fresnel transmission at fiber exit (glass -> air interface)
  4. Geometric angular aperture (which angles hit the detector)
  5. Fresnel transmission at detector (air -> InGaAs, angle-dependent)
Coupling Fraction
  eta = Integral of [ G * T_fiber * T_detector ] over detector angles
  divided by total Gaussian power in forward half-space
  Each factor is evaluated at every angle — not a single average
Dominant Loss Mechanisms
1. Gaussian falloff (dominant)
  Intensity drops exponentially off-axis
  At th0: 13.5% of peak
  At 2*th0: 0.03% of peak
2. Fresnel loss at detector
  High index mismatch (n=1 -> n=3.5)
  Near-grazing incidence in this geometry
  Transmittance 40-60% at typical angles
3. Fresnel loss at fiber exit
  Glass-to-air reflection (~3.6%)
  Relatively minor compared to above two

## Slide 2
How Position Affects Coupling (x, z Dependence)
Vertical distance z (dominant)
  Larger z -> steeper angle from fiber axis
  Steeper angle -> deeper into Gaussian tail -> exponentially less power
  Also: steeper angle -> more grazing on detector -> higher Fresnel loss
  z is the single most critical parameter
Horizontal distance x
  Larger x -> ray angle to detector center decreases (closer to axis)
  -> more Gaussian intensity available
  But also: larger x -> detector subtends smaller angular range
  -> captures less of the beam
  Trade-off: optimal x exists for each z
Combined behavior
  Best coupling at small z and moderate x
  Coupling falls off exponentially with z, logarithmically with x mismatch
Physical Picture
The Gaussian beam is a narrow cone:
most power within ~5 deg of axis.
Moving detector UP (larger z):
  -> requires light at steeper angles
  -> exponential intensity drop
  -> worse Fresnel at detector
Moving detector RIGHT (larger x):
  -> shallower angle (more intensity)
  -> but narrower angular aperture
  -> net effect: diminishing returns
Best 2D coupling: ~4-5%
(-13 to -15 dBm for 0 dBm input)
at z ~ 100-200 um, x ~ 2000-4000 um

## Slide 3
Detector & Waveguide Placement: Safe from Stray Light
Placement Strategy
  All waveguides and detector must lie outside the 2*th0 emission cone
  2*th0 = 10.9 deg contains 99.97% of beam power (only 0.03% beyond)
  Additional 500 um safety margin in lateral (y) direction
Waveguide Loopback
  Lateral shift y = cone height at arm end + 500 um margin
  Arm length 7000 um | pitch 127 um | all arms above the cone
Detector (1 mm diameter, parallel to chip)
  Placed at min. clearance position: 500 um inside WG end, 500 um above cone
  Angle from fiber axis to detector center: 15.1 deg >> 2*th0 = 10.9 deg
  Gaussian intensity at detector: < 10^-7 of peak
  Coupled power: < -80 dBm (effectively zero stray light)
Verification Summary
  Detector center well outside beam cone (15 deg vs 11 deg boundary)
  Waveguides entirely beyond 2*th0 + 500 um margin
  No fiber stray light interferes with detector or waveguide etch region
  Safe for detector operation without additional shielding